Object dection using distance sensor anf LED

// Define pins for ultrasonic and LED
int const trigPin = 4;
int const echoPin = 7;
int const ledPin = 8; // Define a pin for the LED

const int thresholdDistance = 20; // Set the threshold for object detection in centimeters

void setup() {
  Serial.begin(9600);
  pinMode(trigPin, OUTPUT);
  pinMode(echoPin, INPUT);
  pinMode(ledPin, OUTPUT); // Set the LED pin as an output
}

void loop() {
  int duration, distance;

  digitalWrite(trigPin, HIGH);
  delayMicroseconds(10); // Use a short delay to create the pulse
  digitalWrite(trigPin, LOW);

  duration = pulseIn(echoPin, HIGH);
  distance = (duration / 2) / 29.1;
  Serial.println(distance);

  if (distance <= thresholdDistance) {
    // Object detected
    digitalWrite(ledPin, HIGH); // Turn on the LED when an object is detected
  } else {
    // No object
    digitalWrite(ledPin, LOW); // Turn off the LED when no object is detected
  }

  delay(1000);
}

Object dection using distance sensor and Buzzer

// Define pins for ultrasonic, buzzer, and ledpin
int const trigPin = 4;
int const echoPin = 7;
int const buzzerPin = 8; // Define a pin for the buzzer it should be connected to digital pin and analog pin each respectively

const int thresholdDistance = 20; // Set the threshold for object detection in centimeters

void setup() {
  Serial.begin(9600);
  pinMode(trigPin, OUTPUT);
  pinMode(echoPin, INPUT);
  pinMode(buzzerPin, OUTPUT); // Set the buzzer pin as an output
}

void loop() {
  int duration, distance;

  digitalWrite(trigPin, HIGH);
  delayMicroseconds(10); // Use a short delay to create the pulse
  digitalWrite(trigPin, LOW);

  duration = pulseIn(echoPin, HIGH);
  distance = (duration / 2) / 29.1;
  Serial.println(distance);

  if (distance <= thresholdDistance) {
    // Object detected
    digitalWrite(buzzerPin, HIGH); // Turn on the buzzer when an object is detected
  } else {
    // No object
    digitalWrite(buzzerPin, LOW); // Turn off the buzzer when no object is detected
  }

  delay(1000);
}

Gas Sensor
// Define pins for gas sensor and LED
int gasSensorPin = A0;
int ledPin = 13;
bool gasLeakage = false;

void setup() {
  Serial.begin(9600);
  pinMode(ledPin, OUTPUT);
}

void loop() {
  int sensorValue = analogRead(gasSensorPin);
  Serial.print("Gas Sensor Value: ");
  Serial.println(sensorValue);

  if (sensorValue > 200) {
    // Gas is detected (you may need to adjust this threshold)
    Serial.println("1 Gas leakage detected"); // Gas leakage is present
    digitalWrite(ledPin, LOW); // Turn off LED
    gasLeakage = true;
  } else {
    // No gas detected
    Serial.println("0- Gas leakage not detected"); // No gas leakage
    if (gasLeakage) {
      // Only enter this block when transitioning from gas leakage to no gas leakage
      digitalWrite(ledPin, HIGH); // Turn off LED
      gasLeakage = false;
    } else {
      digitalWrite(ledPin, HIGH); // Blink the LED
      delay(500); // Blink for 500 milliseconds
      digitalWrite(ledPin, HIGH);
      delay(500); // Off for 500 milliseconds
    }
  }

  delay(100); // Adjust the delay as needed
}

Temperature Sensor

// Example testing sketch for various DHT humidity/temperature sensors
// Written by ladyada, public domain

// REQUIRES the following Arduino libraries:
// - DHT Sensor Library: https://github.com/adafruit/DHT-sensor-library
// - Adafruit Unified Sensor Lib: https://github.com/adafruit/Adafruit_Sensor

#include "DHT.h"

#define DHTPIN 2 // Digital pin connected to the DHT sensor
// Feather HUZZAH ESP8266 note: use pins 3, 4, 5, 12, 13 or 14 --
// Pin 15 can work but DHT must be disconnected during program upload.

// Uncomment whatever type you're using!
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321
//#define DHTTYPE DHT21 // DHT 21 (AM2301)

// Connect pin 1 (on the left) of the sensor to +5V
// NOTE: If using a board with 3.3V logic like an Arduino Due connect pin 1
// to 3.3V instead of 5V!
// Connect pin 2 of the sensor to whatever your DHTPIN is
// Connect pin 3 (on the right) of the sensor to GROUND (if your sensor has 3 pins)
// Connect pin 4 (on the right) of the sensor to GROUND and leave the pin 3 EMPTY (if your sensor has 4 pins)
// Connect a 10K resistor from pin 2 (data) to pin 1 (power) of the sensor

// Initialize DHT sensor.
// Note that older versions of this library took an optional third parameter to
// tweak the timings for faster processors. This parameter is no longer needed
// as the current DHT reading algorithm adjusts itself to work on faster procs.
DHT dht(DHTPIN, DHTTYPE);

void setup() {
  Serial.begin(9600);
  Serial.println(F("DHTxx test!"));

  dht.begin();
}

void loop() {
  // Wait a few seconds between measurements.
  delay(2000);

  // Reading temperature or humidity takes about 250 milliseconds!
  // Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
  float h = dht.readHumidity();
  // Read temperature as Celsius (the default)
  float t = dht.readTemperature();
  // Read temperature as Fahrenheit (isFahrenheit = true)
  float f = dht.readTemperature(true);

  // Check if any reads failed and exit early (to try again).
  if (isnan(h) || isnan(t) || isnan(f)) {
    Serial.println(F("Failed to read from DHT sensor!"));
    return;
  }

  // Compute heat index in Fahrenheit (the default)
  float hif = dht.computeHeatIndex(f, h);
  // Compute heat index in Celsius (isFahreheit = false)
  float hic = dht.computeHeatIndex(t, h, false);

  Serial.print(F("Humidity: "));
  Serial.print(h);
  Serial.print(F("% Temperature: "));
  Serial.print(t);
  Serial.print(F("°C "));
  Serial.print(f);
  Serial.print(F("°F Heat index: "));
  Serial.print(hic);
  Serial.print(F("°C "));
  Serial.print(hif);
  Serial.println(F("°F"));
}

https://youtu.be/ryri3CRzh8A?si=yG7FyHe-YayKVQWH

IR Sensor

int SensorPin = 9;
int OutputPin = 13;
void setup() {
  pinMode(OutputPin, OUTPUT);
  pinMode(SensorPin, INPUT);
  Serial.begin(9600);
}
void loop() {
  int SensorValue = digitalRead(SensorPin);

  Serial.print("SensorPin Value: ");
  Serial.println(SensorValue);
  delay(1000);
   if (SensorValue==LOW){ // LOW MEANS Object Detected
    digitalWrite(OutputPin, HIGH);
  }
  else
  {
    digitalWrite(OutputPin, LOW);
  }
}

RGB
Counter exp -:
// C++ code
//
int cnt;
void setup()
{
  Serial.begin(9600);
  pinMode(13, OUTPUT);
  pinMode(12, OUTPUT);
  pinMode(11, OUTPUT);
}
void loop()
{
  Serial.println(cnt);
  if(cnt<=10)
  {
    digitalWrite(13, HIGH);
    delay(1000);
    digitalWrite(13, LOW);
    delay(1000);
    cnt++;
  }
  else if(cnt>10 && cnt<=20)
  {
    digitalWrite(12, HIGH);
    delay(1000);
    digitalWrite(12, LOW);
    delay(1000);
    cnt++;
  }
  else if(cnt>20)
  {
    digitalWrite(11, HIGH);
    delay(1000);
    digitalWrite(11, LOW);
    delay(1000);
    cnt++;
  }

}

SOIL MOISTURE SENSOR

Note: Connect cross wires of senors
And align all connection at one side in Arduino
const int sensor_pin = A1;
 /* Soil moisture sensor O/P pin */
void setup() {
Serial.begin(9600);
/* Define baud rate for serial communication */
}
void loop() {
float moisture_percentage;
int sensor_analog; sensor_analog = analogRead(sensor_pin);
moisture_percentage = ( 100 - ( (sensor_analog/1023.00) * 100 ) ); Serial.print("Moisture Percentage = ");
Serial.print(moisture_percentage);
Serial.print("%\n\n");
delay(1000);
}

PIR Sensor
/*
PIR sensor tester
*/
int ledPin = 13; // choose the pin for the LED
int inputPin = 2; // choose the input pin (for PIR sensor)
int pirState = LOW; // we start, assuming no motion detected
int val = 0; // variable for reading the pin status
void setup() {
pinMode(ledPin, OUTPUT); // declare LED as output
pinMode(inputPin, INPUT); // declare sensor as input
Serial.begin(9600);
}
void loop() {
val = digitalRead(inputPin); // read input value
if (val == HIGH) { // check if the input is HIGH
digitalWrite(ledPin, HIGH); // turn LED ON
if (pirState == LOW) {
// we have just turned on
Serial.println("Motion detected!");
// We only want to print on the output change, not state
pirState = HIGH;
}
} else {
digitalWrite(ledPin, LOW); // turn LED OFF
if (pirState == HIGH) {
// we have just turned of
Serial.println("Motion ended!");
// We only want to print on the output change, not state
pirState = LOW;
}
}
}

­